## Slide 1: Optimization-Based Full Body Control for the DARPA Robotics Challenge
Siyuan Feng
Mar. 14 2014

## Slide 2: Introduction
We want a generalized
controller that works
for a variety of tasks.
This is a complex optimization
problem, so we factor it into
two stages.

## Slide 3
NOW
FUTURE
QP
DDP
Full model
Simple model

## Slide 5: Related works
Reference motion generation (Long term)
  Preview control
  Full dynamic programming
  RHC with foot step adjustment
Floating base inverse dynamics (Instantaneous)
  Prioritized inverse dynamics
  Reduced model using CoM and angular momentum
  Orthogonal decomposition

## Slide 6: Outline
Related works
Low level controller
  Inverse dynamics
  Inverse kinematics
State estimation
High level controller
  Walking
  Ladder climbing
  Manipulation
Discussions

## Slide 8: Low level controller
Both inverse dynamics and inverse kinematics
  ID for compliance
  IK to battle modeling errors
ID and IK are formulated as quadratic programming problems optimizing for the current time step.
Based on the full model (floating base)
  Have control over full state
  Easy to specify constraints

## Slide 9: QP formulation
Cost function:
Each row represents an objective:

## Slide 10: Inverse dynamics
Uses desired motions from the high level controller and estimated robot states to compute target acceleration with feedback

## Slide 11: Inverse dynamics
Cost function:
  Target CoM / torso / limb acceleration tracking
  CoP tracking
  Weight distribution
  Change in torque and force
  Regularization
Constraints:
  Equations of motion
  CoP within the support polygon
  Torque limits

## Slide 12: Inverse kinematics
Maintains its own state
Integrate to get
Uses desired motions from high level controller and internal states to compute target velocity with feedback

## Slide 13: State estimation
Simple kinematic filter (EKF) just for pelvis position and velocity estimation
Process model: based on IMU’s acceleration measurement
Observation model: assumes known stationary contact and kinematics

## Slide 14: Outline
Related works
Low level controller
  Inverse dynamics
  Inverse kinematics
State estimation
High level controller
  Walking
  Ladder climbing
  Manipulation
Discussions

## Slide 15
Simulated walking

## Slide 16: Optimizing CoM trajectory
Generates CoM trajectory for a point mass model with Differential Dynamic Programming (DDP)
Uses a nonlinear model

## Slide 17
x vs t
z vs t
y vs t
x vs y

## Slide 18: Atlas static walking

## Slide 19: Atlas static walking
Foot step selection is entirely manual based on a live camera stream.
Toe off is needed for stepping up or long stride
Ankle is purely torque controlled
Integrators
  CoM
  Swing foot

## Slide 20: Atlas ladder climbing

## Slide 21: Atlas ladder climbing
Foot / hand reposition is scripted, but final adjustment is done by the operator.
Intentionally leaning on railings to stop yaw rotation
More kinematic constraint management due to tight spacing between railings

## Slide 22: Atlas full body manipulation

## Slide 23: Remarks about our controller
2-stage setup made concurrent development for multiple tasks possible.
The low level controller is generic enough and seems to be effective for the 3 tasks.
Inconsistency between IK and ID?
  Can bias either solution to the other’s
  Empirically consistent without constraint violation
  Need to reason about the future to steer away from constraints -> can’t be solved at this stage

## Slide 24: Remarks about Atlas
Going slow made things much easier
  Can use integrators
  Delay is not a big deal
Position and torque sensing are pre-transmission
  FK has much more error
  Joint friction is not measured at all
Terms we used in the joint servos
  k_q_p, k_qd_p
  k_f_p, ff_qd is transformed by moment arm

## Slide 25: Next step
Try to model modeling errors / better state estimation
High level controller
  Include angular momentum
  Re-optimize step timing and location based on current state
Low level controller
  Coordinate IK and ID better
  Add a notion of future in QPs through value function
  Valve command in ID?

## Slide 26: Questions?